## Slide 1: Manipulating Electromagnetic Local Density of States by Graphene Plasmonics
Presenter: Wei E.I. Sha
Electromagnetics and Optics Lab
Dept. of EEE, The University of Hong Kong, Hong Kong
Personal Website: http://www.eee.hku.hk/~wsha/
Collaborators：
Dr. Yongpin Chen, University of Electronic Science and Technology
Prof. Jun Hu, University of Electronic Science and Technology
Prof. Li Jun Jiang, The University of Hong Kong

## Slide 2: OUTLINE
1. Significance and History
2. Quantum Electrodynamics
3. Spontaneous Emission, Local Density of States, and Green’s Tensor
4. Graphene Plasmonics to Control the Local Density of States
5. Conclusion

## Slide 3: Why spontaneous emission (decay) is important?
C Walther et al. Science 327, 1495-1497 (2010)
LED (photonic crystal cavity)
Laser (metallic microcavity)
M. Francardi et al. Appl. Phys. Lett.
93, 143102 (2008)
Purcell factor
Control of spontaneously emitted light lies at the heart of quantum optics. It is essential for diverse applications ranging from lasers, light-emitting diodes, solar cells, and quantum information.

## Slide 4: History of spontaneous EMISSION rate
Classical View:
Boltzmann statistics
proportion to photon intensity
spontaneous emission: an exited atom/molecule decay to the ground state and emits a photon

## Slide 5: THREE Regimes in optics
classical optics
ray physics
D>>λ
nano-optics
wave physics
D~λ
quantum optics
quantum physics
D<<λ
At quantum regimes, the object size (<10 nm) is quite small compared to wavelength. In this situation, semi-classical Maxwell-Schrödinger system is required to describe the EM—particle interaction. Moreover, if the number of photons is also quite small, Maxwell’s equations should be quantized.

## Slide 6: A modern interpretation: quantum electrodynamics (1)
Quantized form of Maxwell Equations
Coulomb gauge
Quantized Hamiltonian
eigenmodes
non-interaction part
interaction part
wave function
e: excited state of atom; g: ground state of atom; 0: no photon; 1: one photon
perturbation method could solve it!
wave-particle duality

## Slide 7: A modern interpretation: quantum electrodynamics (2)
Spontaneous emission rate by Fermi golden rule
Mode expansion of dyadic green’s function
Representation by Green’s tensor
Electromagnetic Local density of state (EMLDOS)
Purcell factor

## Slide 8: Graphene
Carbon Nanotubes
Fullerences (C60)
Graphite
Graphene
Physics World 19, 33 (2006)
Atomic thickness;
High optical transmittance and conductivity;
Dynamically modify chemical potentials through tuning the gate voltage
Fabrication

## Slide 9: Formulations for graphene permittivity
Surface conductivity of Graphene given by Kubo formula
Intraband Relaxation
(plasmonic effect)
Interband Transition
(Be neglectable at THz frequencies)
ω-Frequency, µc-Chemical potential, Γ-Carrier scattering rate and T- Temperature;
Where Fermi-Dirac distribution fd is
Converts the surface conductivity to volume conductivity in modeling;
Notes: Due to the forbidden interband transitions by the Pauli blocking, the chemically or electrostatically doped graphene can support strong plasmonic effects particularly at the far-infrared or terahertz regime

## Slide 10: When graphene is applied to control Spontaneous Emission
Quantum Electrodynamics Computational Electromagnetics
Spontaneous Emission Numerical Green’s Function
Low-Dimensional Materials
Electrically Tunable Active Materials

## Slide 11: Graphene vs metal for controlling Spontaneous emission
tunable by chemical potential
sensitive to position
sensitive to polarization
much larger enhancement than metals

## Slide 12: spontaneous Emission in complex multilayer nanostructure
split ring only
split ring + graphene
equivalent principle (PMCHWT) + multilayer Green’s function

## Slide 13: Publications
Pengfei Qiao, Wei E.I. Sha, Wallace C.H. Choy, and Weng Cho Chew, “Systematic Study of Spontaneous Emission in a Two-Dimensional Arbitrary Inhomogeneous Environment,” APS, Physical Review A, vol. 83, no. 4, pp. 043824, Feb. 2011.
Yongpin P. Chen, Wei E.I. Sha, Wallace C.H. Choy, Li Jun Jiang, and Weng Cho Chew, “Study on Spontaneous Emission in Complex Multilayered Plasmonic System via Surface Integral Equation Approach with Layered Medium Green’s Function,” OSA, Optics Express, vol. 20, no. 18, pp. 20210-20221, Aug. 2012.
Yongpin P. Chen, Wei E.I. Sha, Li Jun Jiang, and Jun Hu, “Graphene Plasmonics for Tuning Photon Decay Rate near Metallic Split-Ring Resonator in a Multilayered Substrate,” OSA, Optics Express, vol. 23, no. 3, pp. 2798-2807, Feb. 2015.
Weng Cho Chew, Wei E. I. Sha, and Qi I. Dai, “Green’s Dyadic, Spectral Function, Local Density of States, and Fluctuation Dissipation Theorem,” http://arxiv.org/pdf/1505.01586.pdf

## Slide 14: Conclusion
1. Graphene offers several flexible tuning routes for manipulating EMLDOS, including tunable chemical potential and the emitter’s position and polarization. It shows broadband enhancements of EMLOS compared to metal materials.
2. We study spontaneous emission rate of a quantum emitter near a metallic split-ring resonator, which is embedded in a multilayered substrate incorporating a graphene layer. This design enables a mutual interaction between graphene plasmonics and metallic plasmonics. The boundary element method with a multilayered medium Green’s function is adopted in the numerical simulation.
3. Strong plasmonic coupling with a switch on-off feature was observed, which is helpful to dynamically manipulate spontaneous emission rate in complex optical devices.

## Slide 15: THANKS FOR YOUR ATTENTION!